## Slide 1
AMATEUR DIGITAL VOICE
The Six Modes,
and How to Start
A 30-minute introduction for hams new to the digital modes
Presented by ______________________
Notes: Replace the 'Presented by' line with your callsign and club. Open by asking two questions: who owns a digital radio, and who has actually made a contact with it. The gap between those two hands is the reason this talk exists. The promise: by the end you will know what the six modes are, why they feel harder than they are, and which one to start on. Nobody leaves able to program a radio - that is a different talk.

## Slide 2
AGENDA
What this covers
1
It is really about the internet
The part nobody says out loud
2
Where to point the radio
Two bands, and a surprising reason
3
The six modes
Where each came from, and what makes it itself
4
Six vocabularies, six ideas
Why they feel harder than they are
5
Which one, and how busy is it
The honest answer, including the quiet ones
6
What trips everyone up
Five things that cost people their first evening
Notes: A minute at most. The shape of the talk, so people stop wondering when you will get to the part they came for. If the room is mostly analog operators, say here that everything assumes they know analog and nothing else.

## Slide 3
START HERE
It is really about the internet
The magic is not the modulation. It is that your repeater or hotspot links over the internet to the whole world.
WHAT YOU THINK YOU ARE BUYING
A radio that sounds different
Clearer audio, a screen with names on it, and a mode your friend keeps talking about.
WHAT YOU ARE ACTUALLY BUYING
A door into a network
With a handheld and a decent connection you can hold an ordinary conversation with someone across an ocean — from indoors, on a few milliwatts.
Get your head around that one idea and everything else in this talk follows from it.
Notes: Lead with this, because it reframes everything that comes after. Newcomers arrive thinking digital voice is a modulation scheme. It is a networking hobby that happens to arrive by radio. The few-milliwatts detail lands well. A hotspot puts out a fraction of a watt and reaches the world, which is the opposite of everything an HF operator has spent years learning. If anyone objects that this is 'not real radio' - that is a fair conversation, and the honest answer is that the RF link is short and the network is long. Say so plainly rather than dodging it.

## Slide 4
WHERE IT LIVES
Two bands. That is the whole answer.
Buy a dual-band digital radio and a hotspot and you are equipped for essentially all of amateur digital voice.
70 CENTIMETRES
420 – 450 MHz
Dominant. Most repeaters, nearly all hotspots, all six modes.
2 METRES
144 – 148 MHz
Major. D-STAR, DMR and Fusion repeaters in quantity.
Everything else is a footnote.
33 cm is a real but niche corner. 23 cm is D-STAR's quiet home. 1.25 m deserves better than it gets. Below 6 m there is essentially nothing, and there are good reasons for that.
Notes: Say the short answer first and let people relax. A dual-bander and a hotspot is the right default and almost nobody needs anything else. US allocations shown. Region 1 and Region 3 differ, most noticeably at 70 cm - check your own band plan if the room is not American. The reason nothing lives below 6 m is worth one sentence if asked: a digital voice channel wants 6.25 to 12.5 kHz and an HF SSB channel gives you about 2.8. There is no room. And these are networked modes anyway - they assume infrastructure, which is the opposite of what HF is for.

## Slide 5
WHERE IT LIVES
70 cm did not win on merit
It won because of where somebody else's business happened to be.
1
Commercial land mobile lives at 400–470 MHz
Taxi fleets, utilities, warehouses, public safety — licensed on that band, all of them.
2
So that is where the factories built
Motorola, Hytera, Kenwood and Icom made radios there by the million — and repeaters, duplexers and antennas with them.
3
So that is where the cheap hardware is
New and surplus. A ham buying a 70 cm digital radio is buying into somebody else's economy of scale.
4
So that is where the hobby went
The same story runs at 136–174 MHz, which is exactly why 2 m is the strong second.
Digital voice did not pick its home. It moved in where the rent was cheap.
Notes: People remember this one, because it contradicts what they assume. There is no propagation argument for 70 cm over 2 m for this purpose. The band was chosen by a market that had never heard of us. It also sets up the next section: four of the six modes were not designed for amateur radio either. Same force, different layer. If someone asks about 1.25 m - the propagation is genuinely good and the band is uncrowded. What kills it is that almost nobody manufactures a digital radio for it. The same market logic, running in reverse.

## Slide 6
THE SIX MODES
Six modes, and only one was built for us
Amateur radio has not one digital voice mode but a family of them, each born in a different decade for a different reason.
BORROWED FROM INDUSTRY
DMR · NXDN · P25
Commercial and public-safety standards. Hams adopted them because the radios already existed and were cheap.
BUILT FOR HAMS, BY ONE MAKER
D-STAR · C4FM
D-STAR from JARL and Icom, Fusion from Yaesu. Designed for the hobby — but each with essentially one manufacturer behind it.
BUILT BY HAMS, IN THE OPEN
M17
Open protocol, open codec, open hardware. The only one of the six where the whole stack can be read, studied and changed.
That one distinction explains most of what follows — the vocabulary, the prices, the closed codecs, and why M17 exists at all.
Notes: Give the room this grouping before the six individual slides and they will hang everything on it. The commercial parentage is why DMR talks about talkgroups and colour codes instead of anything a ham would have invented. It is why the radios are cheap. And it is why the vocoders are proprietary - a company licensing a codec to another company had no reason to open it. M17 is not on this slide to sell it. It is here because it is the control experiment: this is what the modes look like when hams design one themselves.

## Slide 7
THE SIX MODES
D-STAR — the pioneer
ORIGIN
JARL and Icom, ~2001
VOCODER
AMBE
SIGNATURE TRAIT
Callsign routing
Where amateur digital voice began. Developed in Japan around the turn of the millennium as an open standard by JARL, the Japanese national society, and brought to market almost entirely by Icom.
Its voice channel carries your callsign in every transmission — which is what makes callsign routing possible. A gateway can route a call to a specific station by their call, anywhere in the world.
Far more common today is linking a repeater or hotspot to a reflector — REF, XRF, DCS and the modern XLX — where many systems meet in one conversation. That architecture is the template every later mode borrowed.
It can sound slightly more robotic than newer modes — the price of being first.
Notes: Treat D-STAR with respect rather than nostalgia. Everything the other five do with reflectors, D-STAR did first. Callsign routing is genuinely unusual and worth ten seconds: you can call a person rather than a place. Almost nobody uses it that way any more, and it is still a lovely idea. The registration step is the thing that stops newcomers, and it comes up again later in the talk. Flag it here in one sentence.

## Slide 8
THE SIX MODES
DMR — the commercial standard hams adopted
ORIGIN
ETSI, 2005
VOCODER
AMBE+2
SIGNATURE TRAIT
TDMA: two conversations, one channel
A European commercial standard, published by ETSI in the mid-2000s for business and professional radio. Hams adopted it for one simple reason: the radios are everywhere and inexpensive.
Its signature trait is TDMA — two time slots alternating on one frequency, so a single repeater carries two independent conversations at the same time. No other mode here does that.
Today it is the most popular amateur digital voice mode, with worldwide networks — BrandMeister, TGIF, FreeDMR and others — organised around talkgroups.
The price of admission is the codeplug. Programming the radio is where nearly everyone gets stuck first, and it is the honest reason some people give up.
Notes: Most of the room will end up on this mode, so give it a little more time than the others. The TDMA point is the engineering highlight of the whole talk. One repeater, one frequency pair, two conversations - a statewide talkgroup on one slot and the club net on the other, same machine, same moment. Do not soften the codeplug warning. Every honest DMR operator in the room already knows it, and pretending otherwise costs credibility with exactly the people who could help a newcomer.

## Slide 9
THE SIX MODES
C4FM / System Fusion — the gentle on-ramp
ORIGIN
Yaesu, 2013
VOCODER
AMBE+2
SIGNATURE TRAIT
AMS: analog and digital share one channel
Yaesu's digital mode, launched in 2013, transmitting C4FM — four-level FSK — and speaking the same AMBE+2 vocoder as DMR.
Its signature trait is Automatic Mode Select. A Fusion repeater or radio hears analog FM and digital C4FM on the same channel and answers each in kind.
That made it the gentlest upgrade path ever offered to a club: replace the analog repeater with a Fusion machine and the analog operators never lose access. Nobody has to be told their radio no longer works.
Networking comes in two flavours — Yaesu's own Wires-X, and the open YSF reflector world the hotspot community built around the protocol. That split confuses newcomers more than anything else about the mode.
Notes: AMS is the feature to dwell on, especially if there are repeater trustees in the room. It is the answer to 'our members will revolt' - they will not, because nothing is taken away from them. The Wires-X versus YSF split is the mode's real complexity. Wires-X is Yaesu's closed network and needs Yaesu hardware; YSF is the open reflector world that hotspots use. Both are Fusion. People assume they are alternatives to each other and get stuck. Fusion is also the easiest mode to get on the air with, which is why it scores so well later in the talk.

## Slide 10
THE SIX MODES
P25 — the public-safety mode
ORIGIN
APCO, 1990s
VOCODER
IMBE (Phase 1)
SIGNATURE TRAIT
Professional gear, professional standard
APCO Project 25 is the North American public-safety digital standard — police, fire and EMS across the continent.
The widely used Phase 1 speaks IMBE on FDMA: one 12.5 kHz channel, one conversation, no time slots. Phase 2 adds two-slot TDMA and AMBE+2, but it is a public-safety feature rarely seen on the ham bands.
Hams run it almost entirely on surplus commercial gear — used Motorola and other public-safety radios that reach the used market as agencies upgrade. That gives the mode its flavour: rugged hardware and a strong crossover with the scanner world.
One quiet advantage: the IMBE patent has expired, so P25 transcodes in free software. No dongle required — which is not true of the AMBE family.
Notes: P25 attracts people who like the equipment. For many the appeal is operating the same iron the professionals carry, and there is nothing wrong with that. State the patent point clearly, because it is counter-intuitive: P25's vocoder is the odd one out, and that turns out to be an advantage. Everything in the AMBE family still wants a licensed chip; IMBE does not. Radios are the barrier - they are pricey, and the user base is small. Be honest about both.

## Slide 11
THE SIX MODES
NXDN — the narrow one
ORIGIN
Icom and Kenwood, ~2006
VOCODER
AMBE+2
SIGNATURE TRAIT
6.25 kHz — the narrowest in common use
A commercial standard developed jointly by Icom, as IDAS, and Kenwood, as NEXEDGE, in the mid-2000s.
Its signature trait is bandwidth. NXDN's narrow mode fits a voice channel into 6.25 kHz — a quarter of a classic 25 kHz analog channel, and half of everything else in this talk.
In the commercial world that meant more channels in the same spectrum. In the amateur world it makes NXDN the quiet efficiency champion — capable, clean, and running on solid surplus hardware.
The honest problem is company. It has one of the smallest operator pools of the six, and a capable mode with nobody on it is still a mode with nobody on it.
Notes: NXDN deserves better than it gets and it is fair to say so, as long as you also say the truth about how few people are on it. The bandwidth figure impresses people once it is in context: four NXDN conversations fit in the space of one old analog channel. Instead of colour codes or DG-IDs it uses a RAN - Radio Access Number. Same idea, different name, which is the whole point of the next section.

## Slide 12
THE SIX MODES
M17 — the open-source newcomer
ORIGIN
The ham community, ~2020
VOCODER
Codec 2 (open)
SIGNATURE TRAIT
Open at every single layer
The youngest mode here and the only one designed by hams, for hams, from scratch — an open-source project started around 2020 by Wojciech Kaczmarski, SP5WWP, and a growing community.
The specification is public, the reference implementations are open source, and — the part that matters most — it uses Codec 2, a free and open vocoder, instead of the patented AMBE family every other mode here depends on.
No licence fees, no proprietary chips, nothing you cannot study or improve. It was built so the transcoding problem would never need a hardware dongle at all.
It is the smallest community here and the one moving fastest. Full-duplex repeater hardware is scarce, so it lives largely on hotspots rather than hilltops.
Notes: Present M17 honestly: it is the smallest, and it is the one you can actually contribute to. Both are true and neither cancels the other. For a club audience the interesting question is not 'should I switch to M17' - it is 'what does it tell us that the open mode had to be built from scratch rather than opened up.' That is a real conversation about the hobby. MMDVM hotspots speak it, OpenRTX brings it to some existing radios, and purpose-built open hardware is appearing.

## Slide 13
THE SIX MODES
All six, side by side
MODE
ORIGIN
VOCODER
SIGNATURE TRAIT
D-STAR
JARL / Icom, ~2001
AMBE
Callsign routing; the original reflector world
DMR
ETSI, 2005
AMBE+2
Two time slots on one frequency; cheap radios
C4FM
Yaesu, 2013
AMBE+2
Analog and digital share one channel
P25
APCO, 1990s
IMBE
The professionals' mode, on surplus pro gear
NXDN
Icom + Kenwood, ~2006
AMBE+2
Ultra-narrow 6.25 kHz channels
M17
Ham community, ~2020
Codec 2
Open source at every layer
Look down the vocoder column. That one column explains more about this hobby than any other fact in this talk — and the next section is why.
Notes: Do not read this table aloud. Put it up, let people photograph it, and point only at the vocoder column. That column is the hinge into the next section. DMR, C4FM and NXDN all speak AMBE+2, so they can share audio freely. D-STAR, P25 and M17 each speak something else, which is why bridging them needs work. If someone wants modulation types, bit rates and occupied bandwidth, send them to the written comparison rather than putting it on a slide.

## Slide 14
THE TRANSLATION
Six vocabularies. About six ideas.
A newcomer is handed Color Code, DG-ID, RAN, NAC, CAN. Five terms, five modes, and nobody says the obvious thing.
They are all the same thing.
Every one of them is the digital descendant of CTCSS — a code that says this transmission is for this system, so a radio can ignore everything else. Five terms collapse into one idea, and you have four fewer things to learn.
The whole of digital voice works like this. There are about six concepts underneath all six modes. What varies is almost entirely the words.
When a DMR operator says “talkgroup” and a D-STAR operator says “reflector module,” they are describing the same room.
Notes: Nothing else in the talk changes how people feel about digital voice as much, so slow down and let it land. The emotional point: newcomers believe they are looking at six things to learn. They are looking at one thing in six dialects. Dialects are easy once you know they are dialects. The next five slides are one concept each. Do not rush them and do not add detail - the whole value is in the simplicity.

## Slide 15
CONCEPT ONE
Who you are
Every transmission has to say who sent it. The modes disagree entirely about what form that answer takes.
DMR
D-STAR
C4FM
NXDN
P25
M17
Identity
DMR ID
Callsign
Callsign
Unit ID
Radio ID
Callsign
Form
a number
—
—
a number
a number
in the stream
The split down the middle is numbers versus callsigns — and it has one enormous consequence.
A number has to be issued by somebody. That is the entire reason RadioID.net exists. If a network routes on numbers, someone must hand them out and prevent collisions. If it routes on callsigns, nobody needs to — yours was issued years ago.
The registry is not a policy choice. It is a mathematical consequence of the identity format.
Notes: Land the consequence line. People treat registration as bureaucracy somebody chose to impose. It is not - it falls straight out of whether the mode routes on numbers or on callsigns. That also predicts the answer for any new mode: tell me how it identifies you and I will tell you whether it needs a registry. ⚠️ One trap to hold until the traps slide: 'Radio ID' means your identity in P25 and a factory hardware serial in C4FM. Same two words, opposite meanings.

## Slide 16
CONCEPT TWO
What lets you in
This row causes more confusion than any other, because people mistake it for the row before it.
DMR
D-STAR
C4FM
NXDN
P25
M17
Access code
Color Code
—
DG-ID
RAN
NAC
CAN
Five different names. One idea. All of them are CTCSS wearing a digital hat.
WHAT IT DOES
A repeater or radio ignores traffic that does not carry the matching code. It is not security — anyone can set it and it is not secret. It is a filter, so two systems sharing a frequency do not open each other's squelch.
THE TRAP
This is a gate, not a badge. It says nothing about who you are. An operator who calls their DG-ID their “Fusion ID” has crossed row one and row two — and that mistake is extremely common.
D-STAR is the odd one out with no access code at all — its gating happens through callsign routing and gateway registration instead.
Notes: Gate, not badge. Say it in those words and repeat it once. If anybody in the room has ever set a CTCSS tone, they already understand this row completely and just do not know it yet. Tell them that - it is a confidence moment. The practical payoff: one wrong digit here and you transmit into silence. No beep, no error, nothing. It is the first thing to check when a radio 'does not work'.

## Slide 17
CONCEPT THREE
The room you are talking in
Where does your voice go once it leaves the repeater? Here the words diverge most violently.
DMR
D-STAR
C4FM
NXDN
P25
M17
Destination
Talkgroup
Reflector
+ module
Room, or
DG-ID
Talkgroup
Talkgroup
Reflector
+ module
Addressed by
a number
a letter
depends
a number
a number
a letter
THREE AND TWO
Three modes call it a talkgroup and address it with a number. Two call it a reflector module and address it with a letter. Different word, same thing: a shared meeting place you connect to and disconnect from.
AND THEN THERE IS C4FM
DG-ID appears in this row and the previous one. On some systems it gates access; on others it also selects the destination. That double duty is real, not a mistake in the table — and it is exactly why C4FM and DMR operators talk past each other.
Notes: Learning to link and unlink is the core operating skill in all of digital voice. Whatever the mode calls it, that is the verb. Point at the C4FM double duty deliberately. It is the single most common source of confusion in that mode and almost nobody explains it - they just answer the question that was asked and leave the person more confused. ⚠️ Hold one more trap for later: 'reflector' is a role, not a standard. D-STAR, M17, YSF and XLX reflectors are all called reflectors and none of them are interchangeable.

## Slide 18
CONCEPT FOUR
The voice itself
Underneath every digital voice mode is a vocoder — the thing that turns speech into bits. It is the hinge the whole digital voice world turns on.
PROPRIETARY — the DVSI AMBE family
OPEN SOURCE
AMBE
AMBE+2
IMBE
Codec 2
D-STAR
DMR
C4FM
NXDN
P25
M17
Ph 1: IMBE
Why some bridges are free: DMR, C4FM and NXDN all speak AMBE+2, so the bits pass straight through.
Why D-STAR is awkward: older AMBE, so the audio must be decoded and re-encoded — and the AMBE family is still licensed, which is why a hardware dongle turns up.
Why P25 is different but not expensive: IMBE's patent has expired, so it transcodes in free software.
Why M17 exists: Codec 2 is free and open from the ground up. It was built so the row would never need a dongle at all.
Notes: If you show one diagram in this talk, show this one. Five of the six modes sit on one company's proprietary lineage. One does not. Read the row and half the mysteries resolve at once - why bridging is sometimes free and sometimes needs hardware, why AMBE dongles exist and cost what they do, and why an open-source community went and wrote a codec of its own. The honest framing: nobody did anything wrong here. A commercial standard licensing a commercial codec is entirely normal. It just has consequences for a hobby built on being able to take things apart.

## Slide 19
CONCEPT FIVE
How the channel is shared
Two radios cannot occupy the same space at the same time. There are only two answers.
TDMA — DMR ALONE
Two conversations take turns
1
2
1
2
1
2
One 12.5 kHz channel, split into two alternating time windows. This is why DMR, alone, has time slots.
FDMA — THE OTHER FIVE
One channel, one conversation
one continuous conversation
D-STAR, C4FM, NXDN, P25 and M17. No slots. Simple, continuous, and exactly how the systems they came from operate.
A time slot is not a digital voice concept. It is a DMR concept.
If you have been hunting for the time slot setting on your Fusion radio, this is why you cannot find it. There isn't one, and there was never meant to be.
Notes: The bottom card answers a question somebody in the room has genuinely spent an evening on. Watch for the nod. P25 Phase 2 does use two-slot TDMA, but it is a public-safety feature and almost never seen on the amateur bands. Mention it only if asked, and say Phase 1 is what hams run. The practical value of TDMA for a club: one repeater, one frequency pair, two independent conversations. A statewide talkgroup on one slot and the local net on the other.

## Slide 20
THE TRANSLATION
Everything, on one screen
DMR
D-STAR
C4FM
NXDN
P25
M17
Who you are
DMR ID
Callsign
Callsign
Unit ID
Radio ID
Callsign
What lets you in
Color Code
—
DG-ID
RAN
NAC
CAN
The room you're in
Talkgroup
Reflector
Room / DG-ID
Talkgroup
Talkgroup
Reflector
The vocoder
AMBE+2
AMBE
AMBE+2
AMBE+2
IMBE
Codec 2
Channel access
TDMA
FDMA
FDMA
FDMA
FDMA
FDMA
Registry needed
Yes
Gateway reg.
No
Yes
Yes — DMR's
No
This is the slide to photograph. Learn the six rows and the vocabularies stop mattering.
When someone says NAC, you hear access code. When someone says Unit ID, you hear identity. When someone says reflector module, you hear the room.
Notes: Pause here and let people take a photograph. Say so out loud - it gives permission and it is the slide they will actually use afterwards. Do not read the table. The value is that it is on one screen, not that it is narrated. The closing line is the point of the whole section: the mode stops being a wall and becomes a dialect. Dialects are easy once you know they are dialects.

## Slide 21
THE TRAPS
Where the words actively mislead you
Two modes using the same word for different things is far more dangerous than two modes using different words for the same thing.
⚠
“Radio ID” means two opposite things
In P25 it is your identity — on the ham bands, your DMR ID. In C4FM it is a factory-burned hardware serial you cannot change and which is not your identity at all.
⚠
DG-ID does two jobs
It gates access and it selects a destination, depending on the system. No other mode's access code does this, and it is the biggest single source of C4FM confusion.
⚠
“Reflector” is not one thing
D-STAR, M17, YSF and XLX reflectors are all called reflectors and none are interchangeable. The word describes a role — a server that fans one transmission out to many — not a standard.
⚠
Not every “ID” is a registration
C4FM asks for none. M17 asks for none. P25 asks for one but it is DMR's. D-STAR registers but issues no number. Only DMR and NXDN work the way a newcomer expects.
Notes: Go through these briskly. The point is inoculation, not depth - if somebody hears the phrase 'Radio ID' next month and hesitates for half a second, this slide did its job. The reflector one matters most in practice, because people buy or configure the wrong thing on the strength of the word. If the room is engaged, expand the DG-ID trap. Everything else can be one sentence each.

## Slide 22
CHOOSING
How busy is each one, honestly
There is no best mode — only the best mode for you, and that usually means whichever one your local repeaters and friends already run.
PEOPLE TO TALK TO — one operator's honest rating, mid-2026
DMR
The busy one — the most people, the cheapest radios, works about everywhere
C4FM / Fusion
The easy one — plug and play, no registration, plenty of activity
D-STAR
The classic — clean audio and solid repeater coverage
P25
The clear one — great audio, pricier radios, a smaller crowd
M17
The open one — smallest crowd, and the one you can contribute to
NXDN
The quiet one — perfectly capable, fewest people on the air
These ratings mix fact and judgment — activity and radio cost are countable, audio quality is not. Treat them as one operator's honest starting point, then go and listen for yourself.
Notes: Be straight about what this chart is. It is a rating, dated mid-2026, from one operator - not a census. There is no clean number for mode popularity, and anybody who gives you one to three decimal places is guessing. The caveat card is not a disclaimer for its own sake. It is the difference between a talk people trust and a talk they argue with. The real advice sits underneath all of it: the mode with the best repeater on your local hill beats the mode with the best specification. Say that.

## Slide 23
CHOOSING
Where the radios actually come from
Two different markets feed this hobby — a new-radio market and a surplus one — and no two modes draw on them the same way.
MODE
NEW
USED / SURPLUS
WHO MAKES THEM
DMR
Many makers, new
Deep — commercial fleet turnover
Baofeng, Radioddity, Retevis · AnyTone, TYT, BTECH · Motorola, Hytera, Kenwood
C4FM
Yes — one maker
Thin
Yaesu
D-STAR
Yes
Modest
Icom, and Kenwood
NXDN
Commercial only
Surplus IDAS and NEXEDGE
Icom (IDAS), Kenwood (NEXEDGE)
P25
Rarely aimed at hams
This IS the market
Retired public-safety gear — Motorola and others
M17
Open hardware, emerging
—
Hotspots, modules, and OpenRTX-flashed radios
For P25 and NXDN, buying used is not the thrifty option — it is essentially the only option.
Notes: The distinction to draw: some modes have a new-radio market aimed at hams, and some have a surplus market aimed at nobody in particular that hams happen to shop in. DMR is the only one that spans both properly, top to bottom, which is most of why it won. Surplus is not a warning. Retired commercial and public-safety radios are built to a standard almost no ham radio meets, and they turn up cheap when an agency re-equips. The trade is programming software, cables, and sometimes band-splits that need checking before you buy. ⚠️ If asked where to buy: the honest answer is the usual ham dealers for new, and eBay, hamfests and club sales for surplus. Do not recommend a specific seller from the front of a room.

## Slide 24
CHOOSING
Cheapest to most expensive
Cheap radios and plenty of choice, rated together — because in practice they arrive together.
DMR
Anything from a budget import to fleet-grade iron. The widest range of any mode, by a distance.
C4FM / Fusion
One maker, so one price ladder — but a real one, from handheld to base.
D-STAR
Icom-centric, and priced accordingly. Fewer bargains than DMR.
M17
Cheap in principle, awkward in practice — hotspots, modules and flashed radios rather than a shelf product.
NXDN
Commercial hardware. Little aimed at hams, so you buy what the fleets retired.
P25
The most expensive way in. Public-safety gear, new or surplus, and it is priced like it.
Longer bar = cheaper radios and more of them to choose from.
Within DMR alone:
budget imports — a working handheld for the price of a nice dinner · the ham sweet spot — AnyTone, TYT, BTECH, with the features you will actually use · commercial iron — Motorola, Hytera, Kenwood, and a deep surplus market behind them
Notes: No prices on this slide, deliberately. A deck that gets re-presented for years should not carry dollar figures that are wrong within a season - and a room full of hams will argue about the numbers instead of listening to the point. The point is the shape: DMR spans everything, P25 is the expensive end, and the three in the middle are middling for different reasons. If someone asks for actual money, give your own current figure out loud and say plainly that it is today's price - do not put it on a slide that leaves the room. The DMR tier card at the bottom is the practical answer to 'what should I buy first'. The middle column is the honest recommendation, and it is fair to say a budget handheld will not perform like one three times the price - that is a reasonable trade if you know you are making it.

## Slide 25
CHOOSING
The honest sheet
MODE
WHAT IT GIVES YOU
WHAT IT COSTS YOU
DMR
Biggest user base and network. Cheap radios from many vendors. Two conversations per channel.
The codeplug is a steep first climb. Easy to overwhelm a brand-new operator.
C4FM
Painless analog-to-digital switching. Beginner and club friendly. No registration.
Effectively a single-vendor mode. The Wires-X versus YSF split confuses people.
D-STAR
First mode built for hams. Callsign routing. Mature worldwide network. Strong data side.
Gateway registration trips up newcomers. Historically Icom-centric. Single slot.
P25
Rugged, public-safety tested. Excellent audio. Transcodes in free software.
Radios are pricey. Small ham user base. More capability than most hams need.
NXDN
Very spectrum-efficient at 6.25 kHz. Clean for small regional networks. Solid hardware.
A small, niche following. Limited radio choice aimed at hams.
M17
Fully open — protocol and codec. No dongle needed. Hackable, and you can contribute.
Newest, with one of the smallest user bases. Limited hardware. Still maturing.
Pick the mode your community is already on, and the cons mostly stop mattering. A smaller network is only a downside if nobody you want to talk to is on it.
Notes: Do not read this table either. Put it up, say the closing line, and move on. It exists so nobody can accuse the talk of selling one mode. If you are asked to pick, the honest answer has two parts: what is on your local hill, and who you already know. Everything else is a tiebreaker. Say the bottom line out loud, because it reframes every 'con' in the table as conditional rather than fatal.

## Slide 26
THE FIRST EVENING
What trips everyone up
Five things, in the order they will bite you.
1
Register first. It is free, and nothing works until you do.
A DMR ID, a D-STAR registration, an NXDN UID. The most common newcomer mistake is keying up before registering and hearing nothing but silence.
2
Match the access codes, or you will hear nothing.
Colour code, DG-ID, NAC, RAN. One wrong digit and you transmit into silence. The radio is not broken.
3
Leave a gap before and between overs.
Internet links and transcoding add a beat of delay. Key up, count one, then speak — or the other operator hears “...anks for the call” instead of your callsign.
Notice what all three have in common: when digital goes wrong, it goes silent. No hiss, no crackle, no error message. Silence is the symptom.
Notes: The bottom card is the single most useful sentence in the talk for a newcomer. Analog fails loudly; digital fails silently. Everything about troubleshooting follows from that. Demonstrate the gap rather than describing it. Key up, count one in your head, then speak. People copy what they see. If the room is DMR-leaning, add the checklist: colour code, time slot, is this talkgroup carried here, is my ID programmed. Nine times out of ten it is one of those four.

## Slide 27
THE FIRST EVENING
Two more, and then go and listen
4
The digital cliff is normal, not a dying radio.
Analog FM fades and gets hissy as it weakens. Digital stays clean right up until it breaks into chirps and vanishes. That sharp edge is expected behaviour, not a fault — and it is why a marginal digital signal feels so much worse than a marginal analog one.
5
It is all in the clear, and keep analog handy.
Part 97 forbids encryption, so digital voice is not private and digital does not mean secret. And since nearly every DV radio also does FM, keep a few analog repeater and simplex channels programmed — they are the universal fallback when the network, or the power, is down.
The codeplug is the real learning curve — not the radio theory.
Programming the radio is where nearly everyone gets stuck. Start by building your own rather than importing somebody else's: a few zones and your hotspot, and learn as you build it.
Notes: The cliff explains a complaint you will hear all evening - 'digital is worse at the edge'. It is not worse, it is different: analog degrades gracefully and digital does not. Whether that is a downside depends entirely on whether you would rather strain through noise or hear nothing. The encryption point catches people out who assume digital implies private. It does not, and on the amateur bands it must not. The codeplug card is the bridge to whatever comes next - a codeplug talk, a build night, or just an offer to sit down with somebody.

## Slide 28
THE NEXT STEP
Before you buy anything — go and listen
Every mode has a live dashboard showing who is transmitting right now. You do not need a radio to use one.
MODE
LISTEN NOW
TO GET ON
DMR
BrandMeister Hoseline — live audio in a browser
Register at RadioID.net
D-STAR
D-STAR Last Heard
Gateway registration required — do it first
C4FM
The YSF Reflector dashboard
No registration — point your hotspot at a reflector
M17
M17Web — reflector traffic in your browser
No registration — set your callsign
NXDN
NXDN North America dashboard
NXDN ID from nxdninfo.com
P25
P25 North America dashboard
Uses your DMR ID — nothing separate
Park on a busy dashboard, listen for a while, then use your radio's echo or parrot to check yourself before you call. Listening first is never wasted time.
Notes: If you have a laptop and a projector, open one of these live during the talk. Thirty seconds of real traffic does more than any slide here. BrandMeister Hoseline is the easiest to demonstrate because the audio plays in a browser with nothing installed. Scheduled nets are the friendliest place for a first check-in - a controlled QSO where somebody is expecting new callsigns. Point people at a net directory rather than telling them to call CQ into a talkgroup cold.

## Slide 29
IF YOU TAKE ONE THING AWAY
Six modes looks like six things to learn.
It is one thing, in six dialects.
Identity, an access code, a room, a vocoder, a way of sharing the channel, and sometimes a registry. Learn those six ideas and every mode becomes a translation exercise instead of a new hobby. Then pick whichever one your local repeater already runs, and go and listen to it.
Questions?
Notes: Close on the idea, not the facts. The room came in believing digital voice was six separate things to learn; send them out knowing it is one thing in six dialects. Then make it concrete in the last sentence: pick what is on your local hill, and go and listen. Nobody should leave this talk about to spend money. If there is time, the best possible ending is to open a dashboard and let the room hear somebody talking.

## Slide 30
TAKE THIS AWAY
Every slide in this talk, written out at length
This deck is free to use, copy, edit and present as your own.
No cost, no copyright, no attribution required. Nothing in it is sponsored and nothing is for sale.
Send your club here when the questions start:
www.n6jet.com — the Digital Voice Guides
Start here
Top Ten Must-Knows · What Bands Is Digital Voice On? · Which Mode Is Right for You?
The six modes
Each Mode Explained (in Brief) · Digital Voice Modes Compared · Pros and Cons
The translation
Rosetta Stone · Access and Squelch Codes · Reflectors and Talkgroups
Then go and listen
Where to Listen · The Digital Cliff · Glossary
Notes: Keep this one. It is not a credit slide - it is the answer to the questions you are about to get asked in the car park. The rows follow the shape of the talk, so whatever somebody is stuck on, one row covers it. Point at the row rather than reading the list. If you would rather not send people to somebody else's site, delete the slide - nothing in the talk depends on it.