## Slide 1
AMATEUR DIGITAL VOICE
What DMR Is,
and How It Actually Works
A 30-minute introduction for operators who already know analog
Presented by ______________________
Notes: Replace the 'Presented by' line with your callsign and club. Open by asking who in the room already runs DMR, and who has a radio still in the box. That tells you how fast to go. The promise of this talk: by the end you will know what DMR is, why it works the way it does, and what it costs you to get started. You will not leave able to program a radio - that is a different talk.

## Slide 2
AGENDA
What this covers
1
Where DMR came from
A commercial standard hams adopted
2
The engineering trick
TDMA, and why one channel carries two conversations
3
Talkgroups and time slots
Why you link instead of tune
4
Why DMR won
Radios, networks and people
5
The honest downsides
The codeplug, and the trap everyone falls into
6
The right way to start
Small, and on purpose
Notes: Keep this to about a minute. The point is to tell people the shape of the talk so they can relax and stop wondering when you will get to the part they came for. If your audience is mostly analog operators, say so here: 'everything in this talk assumes you know analog and nothing else.'

## Slide 3
WHERE IT CAME FROM
DMR was not invented for us
A commercial standard
Published by ETSI, the European telecom standards body.
Designed for fleets, factories and public-safety-adjacent users.
Built to be cheap, rugged and spectrum-efficient.
Hams adopted it, the way we have adopted surplus commercial technology for a century.
Why that matters to you
The radio expects to be programmed, not dialled.
The vocabulary is commercial: talkgroups, colour codes, contacts.
But it also means a worldwide market of radios competing on price.
Nothing about DMR is hard. It is foreign.
Notes: The single most useful thing you can tell a new DMR operator is on the right: it is not hard, it is foreign. Nothing in analog FM prepares you for the idea that the radio has to be programmed before it will do anything. If you get one push-back in the room it will be 'why is it so complicated?' - this slide is the answer. It was built for a company issuing 200 identical radios to a workforce, not for someone spinning a dial.

## Slide 4
HOW IT WORKS
The trick at the heart of it: TDMA
One 12.5 kHz channel is divided into two alternating time windows. Each one carries its own conversation.
1
2
1
2
1
2
1
2
1
2
1
time
Time slot 1 — one conversation
Time slot 2 — a completely separate one
No other amateur digital voice mode does this.
Notes: Slow down here. Everything else in the talk rests on this one piece of engineering. The analogy that works: a single-lane road where two streams of traffic take strict alternating turns, so fast that both feel continuous. A repeater on one frequency pair carries two independent conversations - a statewide talkgroup on slot 1 and the local club net on slot 2, same machine, same antenna, same moment. If someone asks 'does that halve my audio quality' - no. The vocoder is built for it.

## Slide 5
HOW IT WORKS
What that buys you
2
conversations
on one frequency pair,
at the same time
1
repeater
does the work that
used to need two
50%
transmit time
your handheld's PA is
only on half the time
Better battery life on transmit is a real, measurable side effect — not marketing.
Notes: The battery point lands well with anyone who has carried a handheld through a public service event. Half the transmit duty cycle is half the current draw when you are talking. Spectrum efficiency is what got DMR adopted commercially - a company could double its capacity without buying another frequency pair. Hence the radios, and hence the price.

## Slide 6
TALKGROUPS
You do not tune. You link.
ANALOG
Spin the dial and listen
The signal is out there whether you are listening or not.
You can hunt around and discover activity.
Static warns you when you are reaching the edge.
DMR
Choose a conversation
A talkgroup is a conversation, not a frequency.
You only hear the talkgroups you have programmed.
Get a setting wrong and the radio just goes silent. No beep, no error.
Notes: The silent failure on the right is the single biggest source of new-operator frustration. Say it plainly: on DMR, wrong settings do not crackle or hiss. Nothing happens at all. Tell them the fix now so it sticks: when nothing happens, run a short checklist - colour code, time slot, is this talkgroup actually carried here, is my DMR ID programmed. Nine times out of ten it is one of those four.

## Slide 7
TALKGROUPS
Which slot do you use?
R
A duplex repeater
Listens on one frequency and transmits on another, so it can run both slots. Two talkgroups at once — one on TS1, one on TS2.
H
A simplex hotspot
Receives and transmits on the same frequency. With no repeater to supply the TDMA timing reference, it runs one slot only.
On your hotspot, assume time slot 2.
It is a convention of the hotspot software rather than a rule of the standard — but it is close enough to universal that you can rely on it.
Notes: People photograph this one. TS2 on a hotspot is the kind of thing that is obvious once you know it and completely opaque before. Be precise about the honest bit: it is a software convention, not a rule of the DMR standard. But every hotspot you meet will be the same, so in practice it is a rule.

## Slide 8
TALKGROUPS
Static and dynamic talkgroups
Two ways a talkgroup gets connected to you — and the difference explains most of the "why did it go quiet?" questions.
STATIC
Always connected
You attach it permanently, in the network's SelfCare portal.
It is carried all the time, busy or not.
You can hold several on one slot at once.
DYNAMIC
Brought up on demand
You activate it by keying it up.
It drops on its own after about 15 minutes of inactivity.
TAC 310–319 can only ever be dynamic.
Notes: Tell the 'why did it go quiet' story as a story: someone listens to a busy talkgroup, sets the radio down, comes back later and it is silent. They assume something broke. Nothing broke - the dynamic talkgroup timed out exactly as designed. The practical advice: set your regulars static so they are always there, and visit everything else dynamically. The fifteen minutes figure is BrandMeister's. Do not quote it for other networks.

## Slide 9
TALKGROUPS
Not every network works that way
TGIF has no dynamic talkgroups and no inactivity timeout.
You stay parked on the last talkgroup you keyed up — one per time slot — until you deliberately switch.
Why this matters if you run both
The BrandMeister mental model — a few statics that stay, plus a dynamic that times out — simply does not carry over.
Neither does the advice. Anything you read about statics is network-specific.
FreeDMR, AmComm and QuadNet are different again.
Notes: This slide exists to stop someone leaving with one network's rules and applying them everywhere. That mistake costs people an evening. If your club is mostly on one network, say which one and tell them the rest of the talk assumes it.

## Slide 10
TALKGROUPS
Six numbers worth knowing
1
Local
Stays on the repeater. Not linked anywhere.
2
Cluster
A defined group of repeaters — a club, for example.
9
Dial-a-TG
On slot 2 this is the gateway. A poor choice for 'local'.
91
Worldwide
Busy around the clock. The best place to hear traffic.
99
Simplex
Radio to radio, off the network entirely.
9990
Parrot
Plays your own audio back. Nobody else hears it.
Notes: Dwell on Parrot. It is the safest thing a nervous newcomer can do - key up, talk for a few seconds, hear yourself played straight back, and know for certain that the whole chain works. Recommend it as the first transmission anybody makes. Give the TG 9 warning a sentence: people assume 9 means 'local' because it did on some systems. On slot 2 it is the Dial-a-TG gateway, so traffic you think is staying local can go network-wide. Use TG 1 for a true local.

## Slide 11
WHY IT TOOK OVER
Why DMR won: the radios
Because it is a commercial standard with worldwide adoption, hams shop in a market the other modes simply do not have.
Budget imports
Baofeng, Radioddity, Retevis
A working DMR handheld for the price of a nice dinner.
The ham sweet spot
AnyTone, TYT, BTECH
Big channel capacity, GPS, Bluetooth, strong Talker Alias support.
Commercial iron
Motorola, Hytera, Kenwood
Fleet-grade build, and a deep surplus market.
Compare that with System Fusion — Yaesu only — or D-STAR, where the choice is Icom or Kenwood.
Notes: The structural point: DMR radios compete with each other on price and features, and hams pocket the difference. The single-manufacturer modes cannot do that. If someone asks what to buy, the honest answer is the middle column - but say plainly that a thirty-five dollar radio will not perform like a two-hundred-and-fifty dollar one, and that is a fair trade if you know you are making it.

## Slide 12
WHY IT TOOK OVER
Why DMR won: networks, and people
A competitive ecosystem
BrandMeister — the worldwide giant
TGIF — the hotspot-friendly second power
DMR+, FreeDMR, FreeSTAR, AmComm and regional systems
Hundreds of active talkgroups across them
The network effect
New hams go where the activity is. The activity grows because new hams go there.
DMR won the population race years ago, and the lead compounds.
Whatever hour you switch on, somebody is talking.
Notes: Competition among networks, like competition among radios, has improved everything - more features, more bridges, more choice. The honest downside of that multiplicity comes later in the talk: the same talkgroup number can mean different things on different networks. Flag it here in one sentence and promise to come back to it.

## Slide 13
THE FEATURE NOBODY MENTIONS
Talker Alias: a name, not a number
Without it
3107662
With it
N6JET Chris
The transmission itself carries the operator's callsign, embedded in the digital stream.
The old fix was brute force: load a database of the entire worldwide DMR user registry into your radio.
Hundreds of thousands of entries, stale the day you load them, and too big for smaller radios.
With Talker Alias you need no contact list at all. Set your callsign once, and you are a name everywhere you go.
Notes: Nothing else in the talk saves your audience as much work, so give it time. One honest caveat: support varies by radio model and by how networks and repeaters handle the data. Tell people to check Talker Alias capability when they are radio shopping - the AnyTone line is among the strongest here. Replace the example callsign on the right with your own.

## Slide 14
WHY IT TOOK OVER
One radio, the whole digital voice world
DMR
DMR
YSF
D-STAR
NXDN
P25
M17
Through transcoding reflectors, cross-mode functions and network bridges, a DMR radio reaches into all of them.
Notes: DMR has the most cross-mode reach of any digital voice mode. One radio, essentially the whole digital voice world within range. State the payoff out loud: with a well laid out codeplug, one radio and one hotspot do all of it from the channel knob. Networks selected, talkgroups joined, reflectors linked, modes crossed - without ever touching a dashboard. The Pi disappears into the furniture and DMR becomes an all-radio experience, which is the point of ham radio.

## Slide 15
WHAT NOBODY WARNS YOU ABOUT
The honest downside: the codeplug
The codeplug is the price of admission — the steepest first day in amateur radio.
Before your first contact you will meet the programming software and build:
A
Channels
frequency + talkgroup
+ time slot + colour code
B
Zones
channels grouped into
something navigable
C
Contacts
the talkgroups your
radio can call
It is not hard so much as foreign. Nothing in analog FM prepares you for it.
Notes: Do not soften this. Every honest DMR operator in the room already knows it, and pretending otherwise costs you credibility with exactly the people who could help newcomers. The reframe that helps: the codeplug is not a toll you resent paying, it is the tuition that actually teaches you the mode. Put in the time and you get a setup you can troubleshoot, modify and grow - because you built it.

## Slide 16
WHAT NOBODY WARNS YOU ABOUT
And the trap almost everyone falls into
What people do
~1,800
talkgroups downloaded into a brand-new radio, 99% of which they will never key up.
What works
~100
hand-picked across every network you actually use — chosen by you, so every entry means something.
A curated hundred beats an imported sixteen hundred, every time.
Notes: The ~1,800 figure is a count taken from W0CHP's talkgroup list - say so if anyone asks where it comes from. Explain why the big list actively hurts: to reach the one talkgroup you want you scroll through hundreds you do not, the contact list becomes unsearchable, and the radio gets harder to operate rather than easier. This is also the answer to 'DMR is too complicated.' Most of that complexity was downloaded, not required.

## Slide 17
WHAT NOBODY WARNS YOU ABOUT
The rest of the honest list
You must register
A DMR ID is free and quick at radioid.net, but it is one more step before you can transmit.
Text messaging is fragmented
Vendor formats are mutually incompatible in places — commercial fragmentation we inherited.
The vocoder is proprietary
AMBE sits at DMR's heart, which is an irony in a hobby that prizes openness. It is why M17 exists.
Etiquette has commercial manners
Key up, pause, then talk. Leave gaps between overs so linked systems and other operators can get in.
Many networks means confusion
The same talkgroup number can mean different things on different networks.
Notes: Go through these briskly - the point is to be seen to be honest, not to dwell. Demonstrate the key-up-pause-then-talk habit rather than describing it. Key up, count one in your head, then speak. Without it your first word or two gets chopped and the other operator hears '...anks for the call' instead of your callsign.

## Slide 18
IF YOU TAKE ONE THING AWAY
The right way to start
1
One hotspot, one radio
A station you fully control, on your desk, where experiments cost nothing and nobody minds your learning curve.
2
Start on BrandMeister
The biggest user base, the most talkgroups, and the most documentation when you get stuck.
3
One talkgroup to begin
TG 91 Worldwide is busy around the clock. Hearing real traffic proves your setup works.
4
Add one thing at a time
A codeplug scales from a dozen channels to hundreds without ever starting over.
Notes: Whether anyone in the room actually gets on the air is decided here. Land it. Starting small is not a compromise, it is the ideal classroom. You learn the fundamentals on simple gear, make a first contact, and get comfortable - and if DMR clicks for you, you will know exactly what to upgrade and why. And the cost of trying is low. A radio and a hotspot is about the lowest-risk way to try anything in this hobby.

## Slide 19
IF YOU TAKE ONE THING AWAY
Build your own codeplug
The codeplug is not a toll. It is the tuition.
The tempting shortcut is to download somebody else's. Resist it.
A borrowed codeplug hands you hundreds of someone else's decisions — their networks, their talkgroup picks, their zone logic, their naming.
It can still carry their DMR ID, so you transmit under their identity.
And when something breaks you have no idea how to fix it, because you never learned how any of it was put together.
Every channel you create teaches you what a channel is. Every zone teaches you how the radio organises itself.
Notes: In practice, adapting a stranger's codeplug and working out how to use it is more frustrating and takes longer than creating your own. If someone wants a reference it is fine to look at how another operator structured theirs - but type in your own, with your own ID and your own list. One addition: name every channel and zone in a way that makes sense to you. Borrowed codeplugs are full of cryptic names that meant something to whoever built them and nothing to you.

## Slide 20
THE VERDICT
DMR is not the most elegant digital mode,
the most open, or the easiest first hour.
It is the most alive.
The most radios, the most networks, the most talkgroups, the most users, the most bridges to everywhere else — at the lowest cost of entry in digital voice.
Questions?
Notes: Close on the honest version rather than a sales pitch. The room will trust you more for it. Pay the codeplug toll once, keep your talkgroup list curated, and one radio plus one hotspot puts the entire digital voice world on your belt. Leave time for questions. The most common ones: what should I buy, do I need a hotspot if there is a repeater nearby, and how much does it all cost.

## Slide 21
TAKE THIS AWAY
Every slide in this talk, written out at length
This deck is free to use, copy, edit and present as your own.
No cost, no attribution required, no strings attached. Nothing in it is sponsored and nothing is for sale.
Send your club here when the questions start:
www.n6jet.com — the Digital Voice Guides
Getting started
DMR Guide · How to Be Successful with DMR · Hotspot Basics
The confusing bits
Talkgroups & Time Slots · The Codeplug · Scanning with a DMR Radio
When it goes wrong
Troubleshooting · Setting Your TX Audio Level
Notes: Keep this one. It is not a credit slide - it is the answer to the questions you are about to get asked in the car park. The grouping is deliberate: whatever somebody in the room is stuck on, one of those three rows covers it. Point at the row that matches the question rather than reading the list out. If you would rather not send people to somebody else's site, delete the slide - nothing in the talk depends on it.